## Slide 1: LAb1 - RVC

## Slide 2: Goals of the Lab
Requirement engineering
  Analysis
  Formalization (context diagram, FR, ..)
  Consistency

## Slide 3: High level, informal description
Since several years robotic vacuum cleaners (RVC) are available. An RVC is capable of cleaning the floors of a house in autonomous mode.
An RVC system is composed of the robot itself and a charging station. The charging station is connected to an electric socket in the house, and allows charging the battery on board of the robot.
The robot itself is composed of mechanical and electric parts, a computer, and sensors. One infrared sensor in the frontal part recognizes obstacles, another infrared sensor always on the frontal part recognizes gaps (like a downhill staircase). A sensor on the battery reads the charge of the battery. The computer collects data from the sensors and controls the movement of four wheels. Another sensor on one of the wheels computes direction and distance traveled by the robot.
Finally on top of the robot there are three switches: on-off, start, learn.
The learn button starts a procedure that allows the robot to map the space in the house. With a certain algorithm the robot moves in all directions, until it finds obstacles or gaps, and builds an internal map of this space. By definition the robot cannot move beyond obstacles, like walls or closed doors, and beyond gaps taller than 1cm.
The starting point of the learn procedure must be the charging station. When the map is built the robot returns to the charging station and stops.
The start button starts a cleaning procedure. The robot, starting from the charging station, covers and cleans all the space in the house, as mapped in the ‘learn’ procedure.
In all cases when the charge of the battery is below a certain threshold, the robot returns to the charging station. When recharged, the robot completes the mission, then returns to the charging station and stops.
The robot has also a USB port to be used by maintenance staff for diagnostics and possibly firmware update

## Slide 4: 4 documents
Requirements, system level
  Requirements robot
    Requirements firmware
  Requirements charging station

## Slide 5: System Requirements document
Business model
Stakeholders
Context diagram
Functional requirements
NF requirements
Table of access rights
Use cases / scenarios
Conceptual diagram / Glossary
System design
Deployment diagram

## Slide 6: The core functions
Clean house
  Learn space
  Move autonomously

## Slide 7: Business model
Answers those questions
  Who? (customer segments)
    Home segment (no industrial cleaning)
    Basic model ( no app, no internet connection, no alexa..)
  Why? (value proposition)
    Save effort and time to clean house
  Money flow? (revenue stream)
    From users / customers

## Slide 8: Context
Company X developing consumer devices willing to enter market (OEM)
  Termozeta, beghelli
  Philips, Siemens, hoover
  dyson
  Marketing office
  Engineering office ( R&D)
    Software office
    Electronics and mechanical office

## Slide 9: Business model
See Business model canvas

## Slide 10: Stakeholders
End user
Marketing office
  (should know requirements of end users, and define FR NFR for R&D)
R&D office
  Sw developers
All suppliers of components used (tier1)
  Hardware suppliers (memory, cpu, sensors.. )
Floor
Dust
Borders and obstacles
Maintenance staff

## Slide 11: ----- system requirements
Requirements, system level
  Requirements robot
    Requirements firmware
  Requirements charging station

## Slide 12: Context diagram

## Slide 13: Interfaces
Actors | Physical interface | Logical interface
End user | 3 buttons display | Start , learn, clean Various signals (malfunctions)
Power network | Schuko plug | 220v, 50hz
Borders of space and obstacles | IR sensor for obstacle, IR sensor for gap | Recognize obstacle, recognize gap
dust | Air flow | Vacuum generation
floor | wheels | Move
Maintenance staff | Usb port type A | diagnostic Firmware upgrade

## Slide 14: System design
Robot
Charging station

## Slide 15: FR
Sys-FR1 | Manage movement
Sys-FR1.1 | go to charging station (go to position (x,y)
 | go straight
Sys-Fr1.2 | turn
1.3 | stop
1.4 | recognize obstacle
1.5 | 
 | recognize gap
 | compute current position
FR2 | Monitor energy
Sys-FR2.1 | Charge battery
2.2 | Read energy capacity
2.3 | 
 | Switch on / off
 | Clean space
 | Build map of space

## Slide 16: FR
FR3 | Communicate with user
FR | Signal full (of dust)
 | Signal stuck
Fr | Signal energy low
1.3 | 
1.4 | 
1.5 | 
Sys-FR4 | Maintenance
 | Diagnose system
 | upload new firmware
SysFR5 | Clean floor

## Slide 17: Table of rights
 | End user | Maintenance staff |  |  | 
FR1 | Y | Y |  | N | N
FR2 | Y | Y |  | N | N
FR3 | Y | Y |  |  | 
Sys-FR4 | N | Y |  |  | 
FR5 |  |  |  |  | 
FR6 |  |  |  |  | 

## Slide 18: NFR
NFR | Measure
Usability | Any person > 14 yrs old should be able to use system as follows: -first usage: have robot start mapping in < 5 minutes – first usage after mapping: have robot start cleaning in < 1 minute
 | weight <5kg
 | Any person > 14 yrs old should be able to change dust bag in < 2 min
Cost | System should cost < ?? euro
Efficiency | House up to 80sqm should be cleaned in < 1hr Mapping of space, first time, 80 sqm, should take < ?? minutes
 | Should clean efficiently (test: putting 10g of dust on 1sqmeter, after robot passes only 1 g on floor and 9g in dust bag)
safety | No harm to people, animals, things in the house
Reliability | Work for at least 1000 hrs before any component fails
Portability | No (does not apply to system)
maintainability | Possibility to change dust bag
security | No un authorized person should be able to control robot

## Slide 19: Glossary
To be clarified:
  House, Map, space, floor, position, obstacle, gap

## Slide 20: Glossary

## Slide 21: Deployment diagram
Non useful here

## Slide 22: ---- robot requirements
Context diagram
Interfaces
Fr
  R-FR1 Read battery level
  R-FR2 Manage movement
  (TBD, nearly all requirements except part of manage energy are implemented by robot)
Nfr
System design
  4 wheels
  2 engines for moving 2 wheels
  2 engines for rotating 2 wheels
  Ir sensor obstacles
  Ir sensor gaps
  Battery
  Battery Charge sensor
  Computer and firmware
  Dust bag
  Sensor dust bag
  3 buttons
  Led for malfunctions
  Vacuum pump
Requirements, system level
  Requirements robot
    Requirements firmware
  Requirements charging station
Requirement allocation
RFR1 is traced to SYS-FR2.1

## Slide 23: NFR
Usability: same as for system
Cost: same as system minus cost of charging station
Efficiency: same as system
  Translate to: battery at least ??maH
        Consumption of engines…
Safety : same as system

## Slide 24: Context diagram

## Slide 25: Interfaces
Actors | Physical interface | Logical interface
End user | 3 buttons | Start , learn, clean
Charging station | Two pole connector (to be further defined) | 20V dc, max X amp
Borders of space and obstacles | IR sensor for obstacle, IR sensor for gap | Recognize obstacle, recognize gap
dust | Air flow | Generate Vacuum
floor | Wheels | Move, rotate
Maintenance staff | Usb port type A | diagnostic Firmware upgrade

## Slide 26: Deployment diagram

## Slide 27: Use cases and scenarios

## Slide 28: UC1 Clean space
Actor involved: end user
Goal: clean the space
Description: robot moves from charging station, following a path capable of covering the whole space, avoiding obstacle. In each cell the robot cleans dust, then proceeds to next cell. Finally robot returns to charging station
Scenarios: s1, s1V, s1-exc1, ..
exceptions: battery not enough

## Slide 29
S1 (all right, no obstacles)
  Precondition: robot is in charging station, battery is full, robot is working, map of space is available
  Post condition: all cells of space are clean, robot is in charging station
  End user pushes clean button
  Robot starts diagnose procedure, result is ok
  Robot computes path to cover all space (FW-FR1.3) (ex, path is cA1, cA2, c B2,..)
  Robot starts vacuum pump
  Robot moves to Ca1, stays enough time to clean it
  Robot computes and updates its position and orientation
  Robot moves to cA2,
  Robot computes and updates its position and orientation
  …
  Robot back to charging station

## Slide 30
S1V (all right, one obstacle found)
  Precondition: robot is in charging station, battery is full, robot is working, map of space is available
  Post condition: all cells of space are clean, robot is in charging station
  End user pushes clean button
  Robot starts diagnose procedure, result is ok
  Robot computes path to cover all space (FW-FR1.3) (ex, path is cA1, cA2, c B2, cB3)
  Robot starts vacuum pump
  Robot moves to Ca1, stays enough time to clean it
  Robot computes and updates its position and orientation
  Robot moves to cA2,
  Robot computes and updates its position and orientation
  Robot recognizes obstacle in cell cB2 that was not in map. Robot computes turn around of cell cB2, and continues to cB3
  …
  Robot back to charging station

## Slide 31
S1-exc1
  Precondition: robot is in charging station, battery is full, robot is working, map of space is NOT available
  End user pushes clean button
  Robot starts diagnose procedure, result is ok
  Robot does not move, and signals on display to do ‘Learn’

## Slide 32
S1-exc2
  Precondition: robot is in NOT charging station, battery is full, robot is working, map of space is available
  End user pushes clean button
  Robot starts diagnose procedure, result is ok
  Robot does not move, and signals to put it in charging station

## Slide 33
S1-exc3
  Precondition: robot is in charging station, battery is NOT full, robot is working, map of space is available
  End user pushes clean button
  Robot starts diagnose procedure, result is ok
  Robot does not move, and signals on display to do wait to finish charging

## Slide 34
S1-exc4
  Precondition: robot is in charging station, battery is full, robot is NOT working, map of space is available
  End user pushes clean button
  Robot starts diagnose procedure, result is NOK
  Robot does not move, and signals ‘broken, call maintenance’

## Slide 35
S1exc5 (someone moves robot in middle of mission)
  Precondition: robot is in charging station, battery is full, robot is working, map of space is available
  Post condition: robot stops and waits for user intervention
  End user pushes clean button
  Robot starts diagnose procedure, result is ok
  Robot computes path to cover all space (FW-FR1.3) (ex, path is cA1, cA2, c B2,..)
  Robot starts vacuum pump
  Robot moves to Ca1, stays enough time to clean it
  Robot computes and updates its position and orientation
  Robot moves to cA2,
  Robot computes and updates its position and orientation
  ---- someone moves robot
  Robot recognizes map is wrong
  Robot stops and signals on display: ‘bring back to charging station’

## Slide 36
S1exc6 (not enough battery)
  Precondition: robot is in charging station, battery is full, robot is working, map of space is available
  Post condition: space not fully cleaned, robot in charging station
  End user pushes clean button
  Robot starts diagnose procedure, result is ok
  Robot computes path to cover all space (FW-FR1.3) (ex, path is cA1, cA2, c B2,..)
  Robot starts vacuum pump
  Robot moves to Ca1, stays enough time to clean it
  Robot computes and updates its position and orientation
  Robot moves to cA2,
  Robot recognizes not enough charge to finish cleaning
  Robot stops vacuum pump
  Robot computes path P-BACK to charging station
  Robot follows P-BACK

## Slide 37: UC2 Map space
Actor involved: end user
Goal: map the space
Description: robot moves from charging station, applying an algorithm to cover a graph so that all cells are tagged as free or obstacle or gap. In the end the space is described by a map
Scenarios: s2
exceptions: battery not enough, robot breaks, robot not in charging station, map already exists

## Slide 38
S2 (all right, map produced)
  Precondition: robot is in charging station, battery is full, robot is working, map does not exist
  Post condition: map is produced (every cell in space is tagged free, obstacle or gap), robot is in charging station
  End user pushes learn button
  Robot starts diagnose procedure, result is ok
  Robot moves to cell xy applying coverage algorithm
  Cell xy is free (no obstacle found), cell xy is tagged as free in map
  Robot moves to cell kw applying coverage algorithm
  Cell kw is not reachable, cell is tagged as obstacle
  ..
  …(until all cells tried and tagged)
  Robot back to charging station

## Slide 39
S2-exc (map already available)
  Precondition: robot is in charging station, battery is full, robot is working, map exists already
  Post condition:
  End user pushes learn button
  Robot asks ‘are you sure?’
  End user does nothing
  Robot does not move

## Slide 40: ---- charging station requirements
Context diagram
Interfaces
Fr
  Charge battery
Nfr
System design
  Transformer 220v ac to 20v dc
  ..
Requirements, system level
  Requirements robot
    Requirements firmware
  Requirements charging station

## Slide 41: ---- firmware requirements
Context diagram
Interfaces
Fr
  (nearly all robot-fr will be partially or fully allocated here. Ex ‘movement’ is allocated to wheels and wheel engines for actual movement, and to firmware for controlling movements)
Nfr
Glossary
(software design)
Requirements, system level
  Requirements robot
    Requirements firmware
  Requirements charging station

## Slide 42: FR
ID | description | Traced to
FW-FR1 | Manage movement | R-FR2
 | Compute path to charging station Compute energy needed for covering path (path) Compute time needed for covering path (path) | 
 | Build map | 
FW-FR1.3 | computeOptimalPath to cover all map and return to charging station | 
FW-FR1.5 | followPath Reroute in case of obstacle (recompute path) Compute robot position and orientation Recognize that map is wrong (space does not match with map, ex someone has moved the robot) | 
 | moveRobotforward(distance) moveRobotBackward(distance) Stop | 
 | turnRobotRight(degrees) // controls rotation and movement of two wheels to turn robot on the spot turnRobotLeft(degrees) | 
 | Manage Sensors | 
 | Read battery capacity Read max battery capacity Read battery error condition | 
 | Move wheel (id wheel, degrees) | 
 | Rotate wheel (id wheel, degrees) | 

## Slide 43: Context diagram

## Slide 44: Interfaces
Interfaces to be further defined, depending on the actor (component)
Ex the obstacle sensor could be either connected to an interrupt function (interrupt, asynchronous model), or via a memory variable to be read regularly (polling model)
Actors | Physical interface | Logical interface
Button on off |  | Variable Y, true false Start , stop
Button learn |  | 
Ir obstacle sensor |  | Variable Z,
Battery sensor |  | Variable B, long int 0 = 0 charge Maxint = 1Ah Variable Berror, short int 1 =error1 2 = error2 Variable MaxC..

## Slide 45: Embedded system
sensors
logic
actuators

## Slide 46: System process
System Requirements engineering
System Requirement
System design
System design
Software process (requirement, design, implementation, test)
Hardware development (requirement, design, implementation, test)
System integration, test
Software
Hardware
System

## Slide 47: Software process
Requirement engineering
Architecture and design
Implementation
Requirement
document
Design
document
Software
system
Requirement inspection
Design inspection
Test, code inspection
Configuration management
Project management

## Slide 48: System vs sw requirements
System requirements
Functional
  F1
  F2
  F3
Non functional
  NFR1
  NFR2
Software requirements
Functional
  SWF1
  SWF2
  SWF3
Non functional
  SWNFR1
  SwNFR2

## Slide 49: System vs software requirement
System context diagram
Software context diagram